## Slide 1
State-Space Design and Kalman Filter-Based Control of pH Regulation in an Alum Water Treatment System
PROJECT BY
LARICO ANDRES
PRADEEPA HARI
ADITHYA GOVINDARAJAN

## Slide 2
Water Treatment Challenges:
  Removal of impurities via coagulation and flocculation.
  pH regulation critical for efficiency and safety.
Why Alum?
  Neutralizes suspended particles but lowers pH.
  Requires precise dosing and monitoring.

## Slide 3
Objectives
  Develop a control system for accurate pH regulation.
  Incorporate PID and Kalman Filter techniques.
  Ensure stability, fast response, and robustness.
  Address challenges: unmeasured states and sensor noise

## Slide 4
Problem Statement
  Alum addition decreases pH due to acidic flocs.
  Challenges:
    Dynamic system behavior.
    Unmeasured flocculation states.
    Noisy sensor outputs.
  Goal: Design a system to overcome these challenges

## Slide 5
Alum-Based Treatment Process
  Process Overview:
    Alum reacts with water, neutralizing particles.
    Floc formation aids in sedimentation.
  pH Regulation Need:
    Acidic byproducts require correction to meet standards.
    Optimal pH: 6.5–7.5.

## Slide 6
System Dynamics
Key Variables:
Inputs: Alum dosing rate.
States: Suspended solids, flocculated solids, pH.
Outputs: Measured solids and pH levels.
Equations:
State-space representation linking variables.

## Slide 7
State-Space Model
  Mathematical Formulation:
  System Matrices:
    A, B, C, D matrices defined for the treatment system.
  Takeaway:
    Provides a structured approach to control design.

## Slide 8
Controllability and Observability
  Controllability:
    Ensures all states can be influenced by the input.
  Observability:
    Ensures all states can be estimated from outputs.
  Validation:
    MATLAB computations confirm both properties.

## Slide 9
Control Design
  State Feedback Control:
    Stabilizes the system.
    Pole placement ensures desired response.
  Kalman Filter:
    Estimates non-measurable states.
    Handles noisy measurements.

## Slide 10
Pole Placement
Why It Matters:
Determines system stability and response speed.
Chosen Poles: −1,−2,−3.
Balanced trade-off between speed and control effort
.
Simulation Results:
Stable and well-damped response.

## Slide 11
Kalman Filter Design
  Functionality:
    Predicts and corrects state estimates.
  Algorithm Steps:
    Prediction: Estimate next state.
    Update: Correct estimate with measurements.
  Key Benefit:
    Reduces impact of sensor noise.

## Slide 12
System Integration
Control Law:
u(t)=−Kx^(t)+r(t)u(t) = -K\hat{x}(t) + r(t)u(t)=−Kx^(t)+r(t)
Combines state feedback and estimated states.
Result:
Dynamic adjustment of alum dosing for pH control.

## Slide 13
Simulation Setup
  Tools:
    MATLAB and Simulink.
  Components:
    PID controller, state-space plant, Kalman filter.
  Scenarios:
    Desired pH setpoints: 7.0 and 10.0.

## Slide 14
Simulation Results (Setpoint 7.0)
Initial Conditions: [10, 5, 14].
Outcome:
Alum dosing adjusts to stabilize pH at 7.0.
Graph:
True vs. estimated states, alum dosing over time.

## Slide 15
Simulation Results (Setpoint 10.0)
Initial Conditions: Varying from 7.0 test.
Outcome:
System adapts dynamically to maintain pH at 10.0.
Graph:
Show the settling time and overshoot behavior.

## Slide 16
Robustness Analysis
  Disturbances:
    Sensor noise and environmental changes.
  Response:
    Control system remains stable.
    Minimal error in pH regulation.

## Slide 17
Key Takeaways
  Highlights:
    Precise control of pH levels within optimal range.
    Effective use of Kalman filter for noisy measurements.
    Robust performance under disturbances.